### Zeros
### Ones
Свободные члены LSTM
(Long short-term memory Долгая краткосрочная память)

### Constant
0.01 - Свободные члены, если активационная функция ReLU

Если все веса одинаковые, то и поправки будут одинаковыми
 Поэтому
### RandomNormal
keras.initializers.RandomNormal(mean=0.0, stddev=0.05, seed=None)
Initializer that generates tensors with a normal distribution.
Arguments
- mean: a python scalar or a scalar tensor. Mean of the random values to generate.
- stddev: a python scalar or a scalar tensor. Standard deviation of the random values to generate.
- seed: A Python integer. Used to seed the random generator.
### RandomUniform
keras.initializers.RandomUniform(minval=-0.05, maxval=0.05, seed=None)
Initializer that generates tensors with a uniform distribution.
Arguments
- minval: A python scalar or a scalar tensor. Lower bound of the range of random values to generate.
- maxval: A python scalar or a scalar tensor. Upper bound of the range of random values to generate. Defaults to 1 for float types.
- seed: A Python integer. Used to seed the random generator.
### TruncatedNormal
keras.initializers.TruncatedNormal(mean=0.0, stddev=0.05, seed=None)
Initializer that generates a truncated normal distribution.
These values are similar to values from a RandomNormal except that values more than two standard deviations from the mean are discarded and re-drawn. This is the recommended initializer for neural network weights and filters.
Arguments
- mean: a python scalar or a scalar tensor. Mean of the random values to generate.
- stddev: a python scalar or a scalar tensor. Standard deviation of the random values to generate.
- seed: A Python integer. Used to seed the random generator.
### Удобно сохранять зерно датчика случайных чисел, чтобы не сохранять всю сеть.
Когда перебирается несколько сетей.
### VarianceScaling
keras.initializers.VarianceScaling(scale=1.0, mode='fan_in', distribution='normal', seed=None)
Initializer capable of adapting its scale to the shape of weights.
With distribution="normal", samples are drawn from a truncated normal distribution centered on zero, with stddev = sqrt(scale / n) where n is:
- number of input units in the weight tensor, if mode = "fan_in"
- number of output units, if mode = "fan_out"
- average of the numbers of input and output units, if mode = "fan_avg"
With distribution="uniform", samples are drawn from a uniform distribution within [-limit, limit], with limit = sqrt(3 * scale / n).
Arguments
- scale: Scaling factor (positive float).
- mode: One of "fan_in", "fan_out", "fan_avg".
- distribution: Random distribution to use. One of "normal", "uniform".
- seed: A Python integer. Used to seed the random generator.
Raises
ValueError: In case of an invalid value for the "scale", mode" or "distribution" arguments.

[source]
### Orthogonal
keras.initializers.Orthogonal(gain=1.0, seed=None)
Initializer that generates a random orthogonal matrix.
Arguments
- gain: Multiplicative factor to apply to the orthogonal matrix.
- seed: A Python integer. Used to seed the random generator.
References
Saxe et al., http://arxiv.org/abs/1312.6120
### Identity
keras.initializers.Identity(gain=1.0)
Initializer that generates the identity matrix.
Only use for 2D matrices. If the long side of the matrix is a multiple of the short side, multiple identity matrices are concatenated along the long side.
Arguments
gain: Multiplicative factor to apply to the identity matrix.

### lecun_uniform
keras.initializers.lecun_uniform(seed=None)
LeCun uniform initializer.
It draws samples from a uniform distribution within [-limit, limit] where limit is sqrt(3 / fan_in) where fan_in is the number of input units in the weight tensor.
Arguments
seed: A Python integer. Used to seed the random generator.
Returns
An initializer.
References
LeCun 98, Efficient Backprop, - http://yann.lecun.com/exdb/publis/pdf/lecun-98b.pdf
### glorot_normal
keras.initializers.glorot_normal(seed=None)
Glorot normal initializer, also called Xavier normal initializer.
It draws samples from a truncated normal distribution centered on 0 with stddev = sqrt(2 / (fan_in + fan_out)) where fan_in is the number of input units in the weight tensor and fan_out is the number of output units in the weight tensor.
Arguments
seed: A Python integer. Used to seed the random generator.
Returns
An initializer.
References
Glorot & Bengio, AISTATS 2010 - http://jmlr.org/proceedings/papers/v9/glorot10a/glorot10a.pdf
### glorot_uniform
keras.initializers.glorot_uniform(seed=None)
Glorot uniform initializer, also called Xavier uniform initializer.
It draws samples from a uniform distribution within [-limit, limit] where limit is sqrt(6 / (fan_in + fan_out)) where fan_in is the number of input units in the weight tensor and fan_out is the number of output units in the weight tensor.
Arguments
seed: A Python integer. Used to seed the random generator.
Returns
An initializer.
References
Glorot & Bengio, AISTATS 2010 - http://jmlr.org/proceedings/papers/v9/glorot10a/glorot10a.pdf
### he_normal
keras.initializers.he_normal(seed=None)
He normal initializer.
It draws samples from a truncated normal distribution centered on 0 with stddev = sqrt(2 / fan_in)where fan_in is the number of input units in the weight tensor.
Arguments
seed: A Python integer. Used to seed the random generator.
Returns
An initializer.
References
He et al., http://arxiv.org/abs/1502.01852
### lecun_normal
keras.initializers.lecun_normal(seed=None)
LeCun normal initializer.
It draws samples from a truncated normal distribution centered on 0 with stddev = sqrt(1 / fan_in)where fan_in is the number of input units in the weight tensor.
Arguments
seed: A Python integer. Used to seed the random generator.
Returns
An initializer.
References
- Self-Normalizing Neural Networks
- Efficient Backprop
### he_uniform
keras.initializers.he_uniform(seed=None)
He uniform variance scaling initializer.
It draws samples from a uniform distribution within [-limit, limit] where limit is sqrt(6 / fan_in) where fan_in is the number of input units in the weight tensor.
Arguments
seed: A Python integer. Used to seed the random generator.
Returns
An initializer.
References
He et al., http://arxiv.org/abs/1502.01852
An initializer may be passed as a string (must match one of the available initializers above), or as a callable:
from keras import initializers

model.add(Dense(64, kernel_initializer=initializers.random_normal(stddev=0.01)))

# also works; will use the default parameters.
model.add(Dense(64, kernel_initializer='random_normal'))
## Using custom initializers